SCU-2370 37X HIGH RESOLUTION POSITIONING SYSTEM

TECHNICAL SPECIFICATIONS	SECURITY SYSTEM

DIVISION – 28 ELECTRONIC SAFETY AND SECURITY

LEVEL 1__28 20 00 ELECTRONIC SURVEILLANCE

LEVEL 2__28 23 00 VIDEO SURVEILLANCE

LEVEL 3__28 23 29 VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

PART 2 – PRODUCTS

2.01	GENERAL

A.	All equipment and materials used shall be standard components that are regularly manufactured and used in the manufacturer’s system.

B.	All systems and components shall have been thoroughly tested and proven in actual use.

C.	All systems and components shall be provided with the availability of a toll-free (U.S. and Canada), 24-hour technical assistance program (TAP) from the manufacturer.  The TAP shall allow for immediate technical assistance for either the dealer/installer or the end user at no charge for as long as the product is installed.

D.	All systems and components shall be provided with a one-day turnaround repair express and 24-hour parts replacement. The repair and parts express shall be guaranteed by the manufacturer on warranty and nonwarranty items.

2.02	SCU-2370 37X HIGH RESOLUTION POSITIONING SYSTEM

A.	The camera shall provide 1/4” Super HAD color CCD with 600TV lines resolution and a minimum illumination performance to 0.2 Lux @F1.65 in color with 0.0004Lux@F1.65 (Color sens-up).

B. 	The camera shall provide 37x optical zoom (3.5 ~ 129.5mm) and 16x digital zoom.

C.	The camera shall provide 360° continuous rotation with high-speed pan and tilt at 100°/sec, programmable to 255 preset positions.

D.	The camera shall include 2D/3D noise reduction technology, ICR (Infrared Cutfilter Removal), and privacy masking with 12 programmable zones.

2.03	ELECTRICAL SPECIFICATIONS

A.	Input Voltage		24V AC

B.	Power Consumption		80W (Max 140W, heater on)

2.04 	VIDEO SPECIFICATIONS

A. Imaging Device		1/4" Super HAD CCD

B. Total Pixels

1. NTSC 		811(H) x 508(V)

2. PAL		795(H) x (596 (V)

C. Effective Pixels

1. NTSC		768(H) x 494(V)

2. PAL		752 (H) x 582 (V)

D. Scanning System		2:1 Interlace

E. Synchronization		Internal, Line lock

F. Frequency

1. NTSC		15.734KHz (H), 59.94Hz (V)

2  PAL 		15.625KHz (H), 50 Hz (V)

G. Horizontal Resolution		Color: 600 TV Lines in color,  B/W: 700 TV lines

H. Min. Illumination		Color : 0.2Lux (50 IRE@F1.65), 
0.0004 Lux (Sens-up, 512X) 
B/W : 0.02Lux (50 IRE@F1.65)

I. S / N (Y signal) 		More than 50dB

J. I. Video Output		CVBS: 1.0 Vp-p, 75Ω composite

2.05	LENS

A. Zoom Ratio		37x (Optical), 16x (Digital)

B. Focal Length		3.5 ~ 129.5mm (F1.6 ~ 3.9)

C. Max. Aperture Ratio		1:1.6(Wide) ~ 3.9(Tele)

D. Min. Object Distance		1.5 m (4.92 ft)

E. Angular Field of View		55.5°(Wide) ~ 1.59°(Tele) (H)
42.5°(Wide) ~ 1.19°(Tele) (V)

F. Focus		One shot

G. Zoom Movement speed		2.5sec

H. Iris Control		Auto, Manual

2.06 	PAN/TILT

A. Pan Range		360° endless

B. Pan Speed		Preset : 100°/sec

Manual: 0.05°/sec 40°/sec (64 step)

C. Tilt Range		-85° ~ 40°

D. Tilt Speed		Preset: 100°/sec  
Manual: 0.05°/sec ~ 40°/sec (64 step)

E. Preset Positions		255

F. Preset Accuracy		0.1

2.07 	OPERATIONAL SPECIFICATIONS

A. On-Screen Display		English, Spanish, French, German, Italian, Portuguese,
and Chinese

B. Camera Title		On, Off (Displayed 12 characters)

C. Day & Night		Auto (IRC), Color, B/W

D. SSDR		On, Off (level adjustable)

E. Motion Detection		On, Off (8 programmable zones)

F. Backlight Compensation		BLC , HLC, Off

G. Digital Image Stabilization		On, Off

H. Privacy Masking		On, Off (12 programmable zones)

I. 2D+3D Noise Filter (SSNRIII)		On, Off (level adjustable)

J. Sens-up (Frame Integration)		Auto, Off (Selectable 2x ~ 512x)

K. Gain Control		Low, Medium, High, Manual, Off

L. White Balance		AWC, Manual, Indoor, Outdoor, ATW (1,700 ~11,000)

M. Electronic Shutter Speed

1. NTSC		Auto (1/60 ~ 1/120,000sec), Manual, A.FLK

2. PAL		Auto (1/50 ~ 1/120,000sec), Manual, A.FLK

N. Schedule		Day, time schedule

O. Communication		RS-485/422, Coaxial control

P. Protocol		Samsung-T, Samsung-E, Pelco-D, Pelco-P,
Pelco Coaxitron, Panasonic, Honeywell, AD, Vicon, Bosch, GE

Q. Alarm		3 In, 1 Out, 1 Aux

2.08.	ENVIRONMENTAL SPECIFICATIONS

A. Operating Temperature 		-10°C ~ +50°C (+14°F ~ +122°F)

B. Operating Humidity		20% ~ 90% RH

2.09 	MECHANICAL SPECIFICATIONS

A. Dimension (W x H x D)		210 x 590 x 550mm (8.27” x 23.23” x 21.65)

B. Weight		15Kg (33.07 lb)

C. Ingress Protection		IP66

2.10	CERTIFICATIONS

A. SCU-2370N		FCC (Class A), UL/cUL Listed

B. SCU-2370P		CE (Class A), UL/cUL Listed

2.11	WARRANTY

A. 3 years parts and service